## Slide 1
TECHNICAL PRESENTATION
Autonomous Vehicle State
Estimation & Optimal Control
A Nonlinear Bicycle Model, Extended Kalman Filter, and LQR Path-Tracking Framework — Implemented Entirely in Base MATLAB
DYNAMIC BICYCLE MODEL
EXTENDED KALMAN FILTER
LQR PATH TRACKING
MONTE CARLO VALIDATION
Base MATLAB • Zero Toolbox Dependencies • Fully Validated

## Slide 2
OVERVIEW
What We'll Cover
01
The Problem
Why raw sensors alone can't drive a vehicle
02
Objectives
What this project set out to prove
03
System Design
Physics, estimation, and control working together
04
Validation
How the central claim was actually tested
05
Results
What the data shows, across many trials
06
Roadmap
Where the project goes from here
Autonomous Vehicle State Estimation & Optimal Control
2

## Slide 3
THE PROBLEM
Real Sensors Are Noisy, Slow, and Never Enough on Their Own
An autonomous vehicle never sees the world directly, only through imperfect sensors. A controller that trusts raw readings will track poorly and behave unpredictably and even a well-designed controller only ever has an estimate of where the vehicle is, never the ground truth.
1
Noisy, Low-Rate GPS
Fixes arrive at ~10 Hz with meter-scale noise too coarse to steer on directly.
2
Real-Time Control
Steering must be computed every 20 ms, using only what has been estimated so far.
3
Model & Disturbance Uncertainty
Crosswind, road surface, and imperfect actuators mean reality never quite matches the model.
The deeper problem is epistemic, not mechanical:
At every instant, the vehicle has only a belief about where it is built from asynchronous, differently-trusted sensor streams never certain knowledge. That belief has to be good enough, updated fast enough, to close a real-time control loop.
Autonomous Vehicle State Estimation & Optimal Control
3

## Slide 4
OBJECTIVES
Five Goals, Each Independently Verifiable
The project was scoped so every objective could be checked on its own, not taken on faith.
1
Model Reality
Realistic vehicle dynamics, nonlinear tires, and a physical disturbance not an idealized plant.
2
Fuse Sensors
Turn noisy, multi-rate GPS and IMU streams into one trustworthy state estimate.
3
Control Optimally
Track a path using only the estimate, via a hand-derived LQR controller, never the ground truth.
4
Prove the Benefit
Quantify not assume how much fusion actually improves tracking accuracy.
5
Stay Toolbox-Free
Deliver everything, including reports and video, in base MATLAB, zero dependencies.
Autonomous Vehicle State Estimation & Optimal Control
4

## Slide 5
SYSTEM DESIGN
A Closed Sense, Estimate, Control, Act Loop
Sensors
GPS 10 Hz + IMU 50 Hz
Extended Kalman
Filter
State estimate
LQR Controller
Feedback + feedforward
Vehicle Dynamics
Nonlinear bicycle model
estimate feeds back into the filter every step — the loop runs closed, in real time
Autonomous Vehicle State Estimation & Optimal Control
5

## Slide 6
CORE COMPONENT 1 OF 3
Dynamic Bicycle Model
The vehicle is represented as a two-wheel “bicycle” one effective front tire, one effective rear tracking lateral velocity, yaw rate, heading, and position. Tire forces come from a slip-angle model, switchable between a fast linear approximation and the nonlinear Pacejka curve that captures grip saturation at the limit.
State Vector
y, vy, r, psi, X, Y. 6 states
Tire Model
Linear (default) or Pacejka
Integration
RK4, fixed 20 ms timestep
Disturbance
Steering + longitudinal noise, every step
Nonlinear Bicycle
Model
RK4 · 20 ms step
Steering + Accel Cmd
Low-Grip Zones
Disturbance
State: y, vy, r, psi, X, Y
Autonomous Vehicle State Estimation & Optimal Control
6

## Slide 7
CORE COMPONENT 2 OF 3
Extended Kalman Filter
Two asynchronous, differently-trusted sensor streams are fused every step: IMU yaw-rate and acceleration at 50 Hz, GPS position at roughly 10 Hz. The covariance update naturally down-weights whichever source is currently less certain.
PREDICT
Propagate state forward,
grow uncertainty
UPDATE · IMU
Correct heading rate and
accel at 50 Hz
UPDATE · GPS
Correct position whenever
a fix arrives (~10 Hz)
next timestep
Autonomous Vehicle State Estimation & Optimal Control
7

## Slide 8
CORE COMPONENT 3 OF 3
LQR Path Tracking
The tracking-error dynamics are linearized around the current estimated speed, and a discrete-time Riccati equation is solved for the steering gain that minimizes a weighted combination of tracking error and steering effort. A curvature feedforward term is added on top, so the controller doesn't rely on feedback alone to take a known corner.
Q Weight
Penalizes tracking error, larger Q tracks tighter
R Weight
Penalizes steering effort, larger R drives gentler
Gain Caching
Riccati re-solved only when speed drifts, not every step
Feedforward
Curvature term anticipates corners instead of reacting late
Autonomous Vehicle State Estimation & Optimal Control
8

## Slide 9
WHAT SETS THIS APART
Key Highlights
1
Dual Tire Models
Linear and nonlinear Pacejka, selectable, for behavior near the friction limit
2
Parallel UKF
An independent Unscented Kalman Filter cross-checks the EKF's accuracy
3
MPC Alternative
A finite-horizon linear MPC controller, selectable in place of LQR
4
Ghost Vehicle
A second, independently-driven car with live collision-risk prediction
5
Full Validation Suite
No-EKF baseline, Monte Carlo trials, and an LQR sensitivity sweep
6
Zero Toolboxes
Self-tuning animation, video export, and PDF/PPTX reports , all base MATLAB
Autonomous Vehicle State Estimation & Optimal Control
9

## Slide 10
PROVING IT, NOT ASSUMING IT
Validation Methodology
A single favorable run proves very little. Four independent checks close that gap, and none of them can fail silently and take the others down with it.
No-EKF Baseline
Identical controller, re-run headlessly on raw GPS alone
Monte Carlo Trials
24 randomized sensor-noise seeds per controller
LQR Sensitivity Sweep
Steering-effort weight swept across a wide range
Realistic Disturbance
A physical disturbance applied every run, every lap
Validation Report
Autonomous Vehicle State Estimation & Optimal Control
10

## Slide 11
RESULTS 1 OF 3
EKF vs. Raw GPS: Accuracy
Figures below are representative of a typical run; sensor noise and the physical disturbance are randomized every time, so exact numbers vary while the pattern holds.
Chart: Position Error (m)
| EKF | Raw GPS
RMS Position Error (m) | 0.45 | 0.85
Chart: Trials Won (of 24)
| EKF More Accurate | Raw GPS More Accurate
Monte Carlo Trials Won (of 24) | 24 | 0
Autonomous Vehicle State Estimation & Optimal Control
11

## Slide 12
RESULTS 2 OF 3
Monte Carlo Validation: 24 Trials per Controller
The EKF's distribution sits tighter and lower than the raw-GPS distribution across every sampled sensor-noise seed — this is a consistent pattern, not one lucky run.
Chart: RMS Position Error per Trial (m)
| 0.35–0.45 | 0.45–0.55 | 0.55–0.65 | 0.65–0.75 | 0.75–0.85 | 0.85–0.95 | 0.95–1.05
EKF | 9 | 13 | 2 | 0 | 0 | 0 | 0
Raw GPS | 0 | 0 | 1 | 3 | 8 | 9 | 3
Autonomous Vehicle State Estimation & Optimal Control
12

## Slide 13
RESULTS 3 OF 3
LQR Weight Sensitivity: Accuracy vs. Effort
Sweeping the steering-effort weight R reproduces the textbook trade-off curve — confirming the controller's gains came from a principled sweep, not a guess.
Chart: Steering-Effort Weight R
| 50 | 100 | 200 | 400 | 700 | 1200 | 2000 | 3500 | 6000
RMS Cross-Track Error (m) | 1.8 | 1.35 | 1.02 | 0.78 | 0.62 | 0.52 | 0.46 | 0.42 | 0.4
Small R — Aggressive
Large R — Gentle
Autonomous Vehicle State Estimation & Optimal Control
13

## Slide 14
SUMMARY
Key Takeaways
1
Fusion wins decisively
The EKF-driven controller outperformed raw GPS in 24 of 24 matched Monte Carlo trials — not just on average.
2
It's a rate effect, not a bias effect
GPS alone isn't badly biased, it's too slow and sparse to control from directly; 50 Hz effective rate closes the gap.
3
Estimation and control are coupled
The LQR gain schedule depends on estimated speed, so a noisier estimate degrades control beyond position error alone.
4
One run is not proof
The Monte Carlo suite exists because a single comparison is one sample from a random process — it could favor either side by chance.
5
No proprietary tooling required
The complete pipeline — filter, controller, and report writers — runs in base MATLAB.
Autonomous Vehicle State Estimation & Optimal Control
14

## Slide 15
WHERE THIS GOES NEXT
Roadmap
01
Vehicle
Physics
02
State
Estimation
03
Optimal
Control
04
Live
Visualization
05
Validation
Suite
06
Extended
Validation
COMPLETE
PLANNED
✓
Nonlinear vehicle physics with linear and Pacejka tire options
✓
EKF sensor fusion with parallel UKF comparison
✓
LQR path tracking with curvature feedforward, MPC alternative
✓
Live animated dashboard with adaptive real-time pacing
✓
Deterministic video, PDF, PPTX, and JSON export
✓
No-EKF baseline, Monte Carlo trials, LQR sensitivity sweep
Autonomous Vehicle State Estimation & Optimal Control
15

## Slide 16
IMPLEMENTATION
Why Base MATLAB
Every stage of this pipeline — the RK4 integrator, the EKF's Jacobians, the discrete Riccati solve, the video encoder handoff, and even the PDF/PPTX file writers — is implemented from first principles. Nothing depends on a paid toolbox.
NOT REQUIRED
Control System Toolbox
Optimization Toolbox
Robotics System Toolbox
Report Generator Toolbox
BUILT FROM SCRATCH
Vehicle Dynamics & RK4 Integration
EKF / UKF Sensor Fusion
LQR & MPC Control
Animated Dashboard & Video Export
PDF / PPTX / JSON Report Generation
Autonomous Vehicle State Estimation & Optimal Control
16

## Slide 17
THANK YOU
Questions & Discussion
Autonomous Vehicle State Estimation & Optimal Control
Dynamic Bicycle Model • Extended Kalman Filter • LQR Path Tracking • Fully Validated